NETWORK DRIVERS
Network drivers
Network drivers
Thomas Petazzoni
Free Electrons
© Copyright 2009, Free Electrons.
Creative Commons BY-SA 3.0 license
Latest update: Dec 17, 2009,
Document sources, updates and translations:
http://free-electrons.com/docs/network-drivers
Corrections, suggestions, contributions and translations are welcome!

---
Architecture
Architecture
Network stack
net_device
sk_buff
Network hardware driver
Bus infrastructure
(platform, pci, usb, etc.)

---
sk_buff
sk_buff
- The struct sk_buff is the structure representing a network packet
- Designed to easily support encapsulation/decapsulation of data through the protocol layers
- In addition to the data itself, an sk_buff maintains
  - head, the start of the packet
  - data, the start of the packet payload
  - tail, the end of the packet payload
  - end, the end of the packet
  - len, the amount of data of the packet
- These fields are updated when the packet goes through the protocol layers

---
Allocating a SKB
Allocating a SKB
- Function dev_alloc_skb() allows to allocate an SKB
- Can be called from an interrupt handler.
  Usually the case on reception.
- On Ethernet, the size allocated is usually the length of the packet + 2, so that the IP header is word-aligned (the Ethernet header is 14 bytes)
skb = dev_alloc_skb(length + NET_IP_ALIGN);
data, head, tail
length + NET_IP_ALIGN

---
Reserving space in a SKB
Reserving space in a SKB
- Need to skip NET_IP_ALIGN bytes at the beginning of the SKB
- Done with skb_reserve()
skb_reserve(skb, NET_IP_ALIGN);
head
NET_IP_ALIGN
data, tail
length

---
Copy the received data
Copy the received data
- The packet payload must be copied from the DMA buffer to the SKB, using
  - static inline void skb_copy_to_linear_data(struct sk_buff *skb, const void *from, const unsigned int len);
  - static inline void skb_copy_to_linear_data_offset(struct sk_buff *skb, const int offset, const void *from, const unsigned int len);
skb_copy_to_linear_data(skb, dmabuffer, length);
head
NET_IP_ALIGN
data, tail
packet
data
length

---
Update pointers in SKB
Update pointers in SKB
skb_put() is used to update the SKB pointers after copying the payload
skb_put(skb, length);
head
NET_IP_ALIGN
data
packet
data
length
tail

---
struct net_device
struct net_device
- This structure represents a single network interface
- Allocation takes place with alloc_etherdev()
  - The size of private data must be passed as argument. The pointer to these private data can be read in net_device->priv
  - alloc_etherdev() is a specialization of alloc_netdev() for Ethernet interfaces
- Registration with register_netdev()
- Unregistration with unregister_netdev()
- Liberation with free_netdev()

---
struct net_device_ops
struct net_device_ops
- The methods of a network interface. The most important ones:
  - ndo_open(), called when the network interface is up'ed
  - ndo_close(), called when the network interface is down'ed
  - ndo_start_xmit(), to start the transmission of a packet
- And others:
  - ndo_get_stats(), to get statistics
  - ndo_do_ioctl(), to implement device specific operations
  - ndo_set_rx_mode(), to select promiscuous, multicast, etc.
  - ndo_set_mac_address(), to set the MAC address
  - ndo_set_multicast_list(), to set multicast filters
- Set the netdev_ops field in the struct net_device structure to point to the struct net_device_ops structure.

---
Utility functions
Utility functions
- netif_start_queue()
  - Tells the kernel that the driver is ready to send packets
- netif_stop_queue()
  - Tells the kernel to stop sending packets. Useful at driver cleanup of course, but also when all transmission buffers are full.
- netif_queue_stopped()
  - Tells whether the queue is currently stopped or not
- netif_wake_queue()
  - Wake-up a queue after a netif_stop_queue().
    The kernel will resume sending packets

---
Transmission
Transmission
- The driver implements the ndo_start_xmit() operation
- The kernel calls this operation with a SKB as argument
- The driver sets up DMA buffers and other hardware-dependent mechanisms and starts the transmission
  - Depending on the number of free DMA buffers available, the driver can also stop the queue with netif_stop_queue()
- When the packet has been sent, an interrupt is raised. The driver is responsible for
  - Acknowledging the interrupt
  - Freeing the used DMA buffers
  - Freeing the SKB with dev_kfree_skb_irq()
  - If the queue was stopped, start it again
- Returns NETDEV_TX_OK or NETDEV_TX_BUSY

---
Reception, original mode
Reception: original mode
- Reception is notified by an interrupt. The interrupt handler should
  - Allocate an SKB with dev_alloc_skb()
  - Reserve the 2 bytes offset with skb_reserve()
  - Copy the packet data from the DMA buffers to the SKB skb_copy_to_linear_data() or skb_copy_to_linear_data_offset()
  - Update the SKB pointers with skb_put()
  - Update the skb->protocol field with eth_type_trans(skb, netdevice)
  - Give the SKB to the kernel network stack with netif_rx(skb)

---
Reception: NAPI mode (1)
Reception: NAPI mode (1)
- The original mode is nice and simple, but when the network traffic is high, the interrupt rate is high. The NAPI mode allows to switch to polled mode when the interrupt rate is too high.
- In the network interface private structure, add a struct napi_struct
- At driver initialization, register the NAPI poll operation:
  netif_napi_add(dev, &bp->napi, macb_poll, 64);
  - dev is the network interface
  - &bp->napi is the struct napi_struct
  - macb_poll is the NAPI poll operation
  - 64 is the «weight» that represents the importance of the network interface. It limits the number of packets each interface can feed to the networking core in each polling cycle. If this quota is not met, the driver will return back to interrupt mode. Don't send this quota to a value greater than the number of packets the interface can store.

---
Reception: NAPI mode (2)
Reception: NAPI mode (2)
- In the interrupt handler, when a packet has been received:
  if (napi_schedule_prep(&bp->napi)) {
  /* Disable reception interrupts */
  __napi_schedule(& bp->napi);
  }
  - The kernel will call our poll() operation regularly
- The poll() operation has the following prototype
  static int macb_poll(struct napi_struct *napi, int budget)
- It must receive at most budget packets and push them to the network stack using netif_receive_skb().
- If less than budget packets have been received, switch back to interrupt mode using napi_complete(& bp->napi) and re-enable interrupts
- Must return the number of packets received

---
Communication with the PHY (1)
Communication with the PHY (1)
- Usually, on embedded platforms, the SoC contains the Ethernet controller, that takes care of layer 2 (MAC) communication.
- An external PHY is responsible for layer 1 communication.
- The MAC and the PHY are connected using a MII or RMII interface
  - MII = Media Independent Interface
  - RMII = Reduced Media Independent Interface
- This interface contains two wires used for the MDIO bus (Management Data Input/Output)
- The Ethernet driver needs to communicate with the PHY to get information about the link (up, down, speed, full or half duplex) and configure the MAC accordingly

---
Communication with the PHY (2)
Communication with the PHY (2)
SoC
PHY
(R)MII
MAC
Ethernet
connector
MDIO

---
PHY in the kernel
PHY in the kernel
- The kernel provides a framework that
  - Exposes an API to communicate with the PHY
  - Allows to implement PHY drivers
  - Implements a basic generic PHY driver that works with all PHY
- Implemented in drivers/net/phy/
- Documented in Documentation/networking/phy.txt

---
MDIO bus initialization
MDIO bus initialization
- The driver must create a MDIO bus structure that tells the PHY infrastructure how to communicate with the PHY.
- Allocate a MDIO bus structure
  struct mii_bus *mii_bus = mdiobus_alloc();
- Fill the MDIO bus structure
  mii_bus->name = “foo”
  mii_bus->read = foo_mii_bus_read,
  mii_bus->write = foo_mii_bus_write,
  snprintf(mii_bus->id, MII_BUS_ID_SIZE, "%x", pdev->id);
  mii_bus->parent = struct net_device *
- The foo_mii_bus_read() and foo_mii_bus_write() are operations to read and write a value to the MDIO bus. They are hardware specific and must be implemented by the driver.

---
MDIO bus initialization (2)
MDIO bus initialization (2)
- The ->irq[] array must be allocated and initialized. To use polling, set the values to PHY_POLL.
  mii_bus->irq = kmalloc(sizeof(int)*PHY_MAX_ADDR, GFP_KERNEL);
  for (i = 0; i < PHY_MAX_ADDR; i++)
  bp->mii_bus->irq[i] = PHY_POLL;
- Finally, register the MDIO bus. This will scan the bus for PHYs and fill the mii_bus->phy_map[] array with the result.
  mdiobus_register(bp->mii_bus)

---
Connection to the PHY
Connection to the PHY
- The mdiobus_register() function filled the mii_bus->phy_map[] array with struct phy_device * pointers
- The appropriate PHY (usually, only one is detected) must be selected
- Then, connecting to the PHY allows to register a callback that will be called when the link changes :
  - int phy_connect_direct(
    struct net_device *dev,
    struct phy_device *phydev,
    void (*handler)(struct net_device *),
    u32 flags,
    phy_interface_t interface
    )
  - interface is usually PHY_INTERFACE_MODE_MII or PHY_INTERFACE_MODE_RMII

---
Updating MAC capabilities
Updating MAC capabilities
- The MAC and the PHY might have different capabilities. Like a PHY handling Gigabit speed, but not the MAC
- The driver is responsible for updating phydev->advertise and phydev->supported to remove any PHY capability that the MAC doesn't support
- A typical solution for a 10/100 controller is
  - phydev->supported &= PHY_BASIC_FEATURES
  - phydev->advertising = phydev->supported

---
Handling link changes
Handling link changes
- The callback that handle link changes should have the following prototype
  void foo_handle_link_change(struct net_device *dev)
- It must check the duplex, speed and link fields of the struct phy_device structure, and update the Ethernet controller configuration accordingly
  - duplex is either DUPLEX_HALF or DUPLEX_FULL
  - speed is either SPEED_10, SPEED_100, SPEED_1000, SPEED_2500 or SPEED_10000
  - link is a boolean

---
Starting and stopping the PHY
Starting and stopping the PHY
- After set up, the PHY driver doesn't operate. To make it poll regularly the PHY hardware, one must start it with
  phy_start(phydev)
- And when the network is stopped, the PHY must also be stopped, using
  phy_stop(phydev)

---
ethtool
ethtool
- ethtool is a userspace tool that allows to query low-level information from an Ethernet interface and to modify its configuration
- On the kernel side, at the driver level, a struct ethtool_ops structure can be declared and connected to the struct net_device using the ethtool_ops field.
- List of operations: get_settings(), set_settings(), get_drvinfo(), get_wol(), set_wol(), get_link(), get_eeprom(), set_eeprom(), get_tso(), set_tso(), get_flags(), set_flags(), etc.
- Some of these operations can be implemented using the PHY interface (phy_ethtool_gset(), phy_ethtool_sset()) or using generic operations (ethtool_op_get_link() for example)

---
Statistics
Statistics
- The network driver is also responsible for keeping statistics up to date about the number of packets/bytes received/transmitted, the number of errors, of collisions, etc.
  - Collecting these informations is left to the driver
- To expose these information, the driver must implement a get_stats() operation, with the following prototype
  struct net_device_stats *foo_get_stats
  (struct net_device *dev);
- The net_device_stats structure must be filled with the driver. It contains fields such as rx_packets, tx_packets, rx_bytes, tx_bytes, rx_errors, tx_errors, rx_dropped, tx_dropped, multicast, collisions, etc.

---
Power management
Power management
- To support suspend and resume, the network driver must implement the suspend() and resume() operations
- These operations are referenced by the xxx_driver structure corresponding to the bus on which the Ethernet controller is
- The suspend() operation should
  - Call netif_device_detach()
  - Do the hardware-dependent operations to suspend the devices (like disable the clocks)
- The resume() operation should
  - Do the hardware-dependent operations (like enable the clocks)
  - Call netif_device_attach()

---
References
References
- «Essential Linux Device Drivers», chapter 15
- «Linux Device Drivers», chapter 17 (a little bit old)
- Documentation/networking/netdevices.txt
- Documentation/networking/phy.txt
- include/linux/netdevice.h, include/linux/ethtool.h, include/linux/phy.h, include/linux/sk_buff.h
- And of course, drivers/net/ for several examples of drivers
- Driver code templates in the kernel sources:
  drivers/usb/usb-skeleton.c
  drivers/net/isa-skeleton.c
  drivers/net/pci-skeleton.c
  drivers/pci/hotplug/pcihp_skeleton.c

---
Practical lab - Network drivers
Practical lab – Network drivers
Implement a working network driver for the MACB Ethernet controller of the AT91SAM9263 CPU