PCI driver registration
Objective: Get familiar with PCI device and driver registration
After this lab, you will be able to
- Register devices supported by a PCI driver
- Register a PCI driver
- Enable a PCI device and request the I/O port and memory regions used by the device.
## Setup
Go to the /home/<user>/felabs/linux/pci directory.
Install the qemu package if you don't have it yet:
sudo apt-get install qemu
Compile a Linux 2.6.36 kernel for x86 with the configuration file provided in the data/ subdirectory, and boot it through NFS on the nfsroot/ directory, using the supplied run_qemu script.
We are going to work with the ens1370.c driver available in nfsroot/root/. Check that the existing template driver compiles and loads well.
## PCI questions
What's the IRQ line used by this audio card device?
Find the IRQ number from userspace in your virtual system.
Find the vendor and device ids for the card, and declare the supported device in the driver code.
Also find these ids from userspace.
## PCI driver registration
Register the pci driver, and see your new driver in /sys/bus/pci/drivers.
Add the calls to the pci_enable_device() and pci_disable_device() functions, and see a message in the console confirming the IRQ assigned to your device.
Reserve all the I/O ports for your device and see these reservations in /proc.