Lab – Using USB Gadget drivers
Objective: Configure and compile a kernel for USB gadget usage. Test and experiment with serial, Ethernet and block USB gadget drivers.
## Setup
Go to the /home/<user>/felabs/usbgadget/usage/ directory.
## Kernel configuration, compilation and installation
Grab a recent kernel version and configure it with the configuration file provided in the data/ directory.
Run your favorite kernel configuration utility (xconfig, gconfig or menuconfig) and add support for USB Gadget. It should include:
- Core USB Gadget support, statically compiled
- AT91 USB Gadget controller support, statically compiled
- Serial, Ethernet and storage USB Gadget drivers, compiled as modules
Compile your kernel with make, then generate the uImage with make uImage and install the modules in the root filesystem (in the nfsroot/ directory) using make modules_install. Hint: don't run make modules_install as root, and use the INSTALL_MOD_PATH variable.
## Boot the board
Boot the Calao board with the root filesystem mounted over NFS. The filesystem in /home/<user>/felabs/usbgadget/usage/nfsroot/ should be mounted as the root filesystem. It should contain the USB gadget driver modules in /lib/modules/<kernelversion>/.
## Using the Ethernet gadget driver
Load the g_ether kernel module with the modprobe command. You should see a new usb0 network interface with ifconfig. Set an IP address such as 192.168.42.2 to this new interface. Then connect the Calao board to your development workstation using the USB device cable. Ubuntu will automatically detect the new device, load the driver, and create the network interface. You can then use NetworkManager to configure a static IP address such as 192.168.42.1 to this new usb0 interface.
We have now established an Ethernet over USB connection, that can be used as usual. You can for example test it with ping. Because our root filesystem is mounted over NFS, we cannot disconnect the Ethernet cable, but if our system was flashed into the NAND of the Calao board, then we could remove this Ethernet cable.
Using the storage gadget driver
On your host workstation, prepare a filesystem image that will contain the filesystem made visible by the Calao board through the USB connection. To do so:
- Create an empty file of 10 megabytes
  dd if=/dev/zero of=disk.img bs=1M count=10
- Format it as FAT
  mkfs.vfat -F disk.img
- Transfer it to the root directory of the Calao board filesystem
  mv disk.img nfsroot/root/
Now, on the Calao board, load the USB Storage gadget driver and tell it to use disk.img as the file containing the data to export:
modprobe g_file_storage file=/root/disk.img
Then connect the device to your development workstation. Ubuntu will automatically detect the device, load the driver, mount the filesystem and display a nice list of the files present in the device.
## Using the serial gadget driver
Load the g_serial kernel module on the Calao board. Then, create the /dev/ttyGS0 device file that correspond to the major and minor number as given by the file in sysfs (see the training slides for details).
Now, connect the Calao board to your development workstation using the USB device cable. Your Linux system will automatically detect the new USB device cable and create the /dev/ttyACM0 device file.
Now, to make a simple test:
- Run cat /dev/ttyACM0 on your workstation
- And run echo “hello world” > /dev/ttyGS0 on your device
You can also test the opposite communication (cat on the device and echo on your workstation). These are very simple tests, but they show that the serial communication is working. It means that we could run an application on our device that opens /dev/ttyGS0 and makes features available to the workstation through the serial port.