FLASH FILESYSTEMS
Embedded Linux Conference Europe 2010
Flash
filesystem
benchmarks
Michael Opdenacker
Bootlin
© Copyright 2010, Bootlin.

---
Company info
Bootlin
Bootlin
Free embedded Linux and kernel materials
https://bootlin.com/docs
Linux BSPs, device drivers and plumbing
Buildroot
http://buildroot.org

---
Questions
Questions
Who uses?
- jffs2
- ubifs
- yaffs2
- logfs
- nftl?

---
Introduction
Introduction
- Work started in 2008 at ELC-E
  Showed benchmarks on jffs2, yaffs2 and ubifs
- What has happened during the last 2 years
  - Project continued with funding from the CE Linux Forum
  - Automation scripts now supporting multiple boards
  - New armel root filesystem for the tests (replaces Buildroot).
    Easier access to MTD and filesystem utilities.
    Udev simplifies the use of UBIFS.
  - Now measuring driver initialization time through loading external modules (instead of static drivers - boot time was not measured).
  - LogFS mainlined in 2.6.34

---
jffs2
jffs2
http://www.linux-mtd.infradead.org/doc/jffs2.html
- Today's standard filesystem for MTD flash
- Nice features: on the fly compression (saves storage space and reduces I/O), power down reliable, wear-leveling and ECC.
- Drawbacks: doesn't scale well
  - Mount time depending on filesystem size:
    the kernel must scan the whole filesystem at mount time, to read which block belongs to each file.
  - Need to use the CONFIG_JFFS2_SUMMARY kernel option to store such information in flash. This
    dramatically reduces mount time (from 16 s to 0.8s for a 128 MB partition).
Standard file
API
JFFS2
filesystem
MTD driver
Flash chip

---
yaffs2
yaffs2
Standard file
API
http://www.yaffs.net/
- Mainly supports NAND flash
- No compression
- Wear leveling, ECC, power failure resistant
- Fast boot time
- Code available in a separate git tree
  Should be included in the mainline kernel
  soon.
YAFFS2
filesystem
MTD driver
Flash chip

---
UBI (1)
UBI (1)
Unsorted Block Images
- http://www.linux-mtd.infradead.org/doc/ubi.html
- Volume management system on top of MTD devices.
- Allows to create multiple logical volumes
  and spread writes across all physical blocks.
- Takes care of managing the erase blocks and wear leveling. Makes filesystem easier to implement.

---
UBI (2)
UBI (2)
Volume1
Volume2
UBI
Logical
Erase Blocks
LEB
LEB
LEB
LEB
LEB
LEB
LEB
MTD
Physical
Erase Blocks
PEB
PEB
PEB
PEB
PEB
PEB
PEB
PEB
PEB
Free block
Free block

---
UBIFS
UBIFS
http://www.linux-mtd.infradead.org/doc/ubifs.html
- The next generation of the jffs2 filesystem,
  from the same linux-mtd developers.
- Available in Linux 2.6.27
- Works on top of UBI volumes
- Has a noticeable metadata overhead on very small partitions (4M, 8M)
Standard file
API
UBIFS
UBI
MTD driver
Flash chip

---
LogFS
LogFS
http://en.wikipedia.org/wiki/LogFS
- New comer in mainline (integrated in 2.6.34)
- Still experimental (at least in 2.6.36)
- Designed to be very fast at mount time
  (even faster than UBIFS): O(1) mount time
- Supposed to consume less RAM than JFFS2
- Ability to run on block devices but with poor performance

---
Logfs in action
Logfs in action
kernel BUG at fs/logfs/segment.c:858!
Unable to handle kernel NULL pointer dereference at virtual address 00000000
pgd = ced00000
[00000000] *pgd=8edbd031, *pte=00000000, *ppte=00000000
Internal error: Oops: 817 [#1]
last sysfs file: /sys/devices/virtual/vc/vcsa6/uevent
Modules linked in: logfs zlib_deflate
CPU: 0 Tainted: G W (2.6.36 #2)
PC is at __bug+0x1c/0x28
LR is at __bug+0x18/0x28
pc : [<c002b428>] lr : [<c002b424>] psr: 20000013
sp : cfb7fe38 ip : 00000928 fp : 00000080
r10: c0580b20 r9 : 00000009 r8 : ffffffff
r7 : cfb7fea4 r6 : 00000080 r5 : cf50cd58 r4 : c0580b20
r3 : 00000000 r2 : cfb7fe2c r1 : c02fd4b7 r0 : 0000002c
Flags: nzCv IRQs on FIQs on Mode SVC_32 ISA ARM Segment user
Control: 10c5387d Table: 8ed00019 DAC: 00000015
Process umount (pid: 868, stack limit = 0xcfb7e2e8)
Stack: (0xcfb7fe38 to 0xcfb80000)
fe20: bf0122dc bf0122ec
With Linux 2.6.36.
Reported on the linux-embedded ML

---
SquashFS
SquashFS
http://squashfs.sourceforge.net/
- Filesystem for block storage, so it doesn't support the MTD API.
- However, as it is read-only, it works fine with mtdblock,
  as long as the flash chip doesn't have any bad blocks.
- You could use it for read-only sections in your filesystem,
  but you cannot rely on it (bad blocks can always happen).

---
Benchmark hardware (1)
Benchmark hardware (1)
Calao Systems USB-A9263
- AT91SAM9263 ARM CPU
- 64 MB RAM
  256 MB flash
- 2 USB 2.0 host
  1 USB device
- 100 Mbit Ethernet port
- Powered by USB!
  Serial and JTAG through
  this USB port.
- Multiple extension boards.
- Approximately 160 EUR
Supported in mainstream Linux since version 2.6.27!

---
Benchmark hardware (2)
Benchmark hardware (2)
TI Beagle Board
- TI OMAP 3530 ARM CPU
- 256 MB RAM, 256 MB flash
- RS-232 serial
- USB Host
  USB OTG
- JTAG
- DVI-D, S-Video
- Audio In and Out
- MMC/SD
- Only 150 USD

---
Benchmark methodology
Benchmark methodology
Using a Debian Squeeze root filesystem for armel.
- Supports armv4 (Ubuntu on arm only supports v7)
- Contains all the tools to manipulate flash,
  as well as utilities for each filesystem.
Using automated scripts supporting multiple boards
- Take care of sending commands to the boards
  through a serial line.
- Test rootfs and GPL scripts available on
  https://bootlin.com/pub/utils/board-automation/

---
Initialization tests
Initialization tests
- Time to load the filesystem drivers
- Special case of UBIFS:
  - ubi module initialization
  - ubiattach time
  - ubifs module loading time

---
Initialization benchmarks
Initialization benchmarks
CALAO Board
Partition size
Time
Beagle Board
Partition size
Time
Note: couldn't measure ubifs on Beagle (bug)

---
ubifs issue on Beagle
ubifs issue on Beagle
Methodology:
- ubiattach, mount, file, detach, attach again... oops
- No problem on Calao!
...
UBI error: ubi_io_read: error -74 (ECC error) while reading 64 bytes from PEB 53:0, read 64 bytes
UBI error: ubi_io_read: error -74 (ECC error) while reading 64 bytes from PEB 54:0, read 64 bytes
UBI error: ubi_io_read: error -74 (ECC error) while reading 64 bytes from PEB 62:0, read 64 bytes
UBI error: ubi_io_read: error -74 (ECC error) while reading 64 bytes from PEB 63:0, read 64 bytes
UBI warning: check_what_we_have: 29 PEBs are corrupted
corrupted PEBs are: 3 4 8 10 11 13 14 15 18 20 21 23 24 25 29 33 34 35 36 38 39 40 41 44 50 51 53 62 63
UBI error: check_what_we_have: too many corrupted PEBs, refusing this device
ubiattach: error!: cannot attach mtd1

---
mount time benchmarks
mount time benchmarks
CALAO Board
Partition size
Time
Beagle Board
Partition size
Time
Note: couldn't measure ubifs on Beagle (bug)

---
init + mount time benchmarks
init + mount time benchmarks
CALAO Board
Partition size
Time
Beagle Board
Partition size
Time
Note: couldn't measure ubifs on Beagle (bug)

---
init + mount memory usage
init + mount memory usage
CALAO Board
Partition size
RAM (KB)
Beagle Board
Partition size
RAM (KB)
Note: couldn't measure ubifs on Beagle (bug)

---
used space
Used space
CALAO Board
Partition size
Space (KB)
Beagle Board
Partition size
Space (KB)
Note: data missing on Beagle (bug to investigate)

---
Read time benchmarks
Read time benchmarks
CALAO Board
Partition size
Time
Beagle Board
Partition size
Time
Note: couldn't measure ubifs on Beagle (bug)

---
Remove time benchmarks
Remove time benchmarks
CALAO Board
Partition size
Time
Beagle Board
Partition size
Time
Note: couldn't measure ubifs on Beagle (bug)

---
Write time benchmarks
Write time benchmarks
CALAO Board
Partition size
Time
Beagle Board
Partition size
Time

---
Video write time benchmarks
Video write time benchmarks
CALAO Board
Partition size
Time
Beagle Board
Partition size
Time

---
Flash filesystems conclusions
Flash filesystem conclusions
logfs
Unusable so far. Crashes on both Beagle and Calao boards (2.6.36).
jffs2
- Poor performance compared to the others.
- May only make sense on small partitions where space matters.
yaffs2
- Best choice for write performance.
- Good choice for small partitions when read/write performance and boot time matter more than space.
- Show get in mainline in the next months
ubifs
Good or best performance in medium and big partitions
Time to replace your jffs2 partitions by ubifs or by yaffs2!

---
Future of MTD devices?
Future of MTD devices?
Embedded MMC (eMMC) starting to replace NAND flash
- Cheaper: ~30 EUR for 8 GB (Source: Calao Systems)
- Bad blocks managed internally
  No more issue with the bootloader sector going corrupt.
- Wear leveling could apply to the whole storage space
  (In theory, like with UBI. Not true with some devices).
- Automatic sleep mode
- Faster boot time: driver-less initialization.
- Can take advantage of block filesystems
  with optimizations for SSDs.
- How reliable, trustworthy and resistant are these?
  Loosing control on wear leveling.

---
Quick block fs benchmarks
Quick block fs benchmarks
Methodology
- Tests run on the Beagle board
- Copy 800 MB of rootfs files from USB to MMC
- Flush caches
- Read MMC contents
- Flush caches
- Remove MMC contents
- Write 100 copies
  of a 6 MB video to MMC

---
Disk usage after format
Disk usage after format
Filesystem
Space (MB)

---
MMC copy from USB (ext3)
MMC copy from USB (ext3)
Filesystem
Time (s)

---
MMC read time
MMC read time
Filesystem
Time (s)

---
MMC remove time
MMC remove time
Filesystem
Time (s)
jfs: 2872s!	xfs: 239s!

---
MMC write video time
MMC write video time
Filesystem
Time (s)

---
MMC video write speed (MB/s)
MMC video write speed (MB/s)
Filesystem
MB/s

---
Block storage: conclusions
block storage: conclusions
- ext4 is great!
  Best compromise between maturity and performance.
- btrfs rocks!
  Though not production ready (still experimental).
- xfs is very disappointing
  (it has good performance on rotating disks)
- Hard to tell which filesystem will work best on your system.
  Make your own experiments (switching filesystems is cheap)!

---
Call for change
Call for change
- Squashfs on top of UBI
  Too much overhead today
- Block device on top of UBI
- Yaffs2 in mainline!
- Merge the Logfs Forum with the MTD Foundation ;-)
SquashFS
MTD block
 MTD API
UBI
MTD driver
Flash chip

---
Thanks - Questions
Thanks!
Questions?
Comments?
Comments?
Comments?
Comments?
Scripts and test root filesystem on https://bootlin.com/pub/utils/board-automation/

---
Flash fs mini-BOF
Flash fs mini-BOF
- Do you think that eMMC will completely replace NAND flash?
- Would you feel comfortable to use block flash storage
  as a swap area?
- How do you limit the number of writes in a read/write partition?
- Any project you would like CELF to support?